## Slide 1
Group Members :
Group Number:
PRE-DECODER
AND
COLUMN DECODER DESIGN
7
MT25111 Charu Singh
MT25130 Neeti Mishra
MT25157 Vishal Kumar Singh
Course:- Memory Design And Test
Prof.: Dr Anuj Grover

## Slide 2: Problem Statement
Requirements :
To design a pre-decoder with the following
Input capacitance <10fF
Output loading is for 512 rows,
Hold time to be negative at FF/1.32/-40,
Setup time to be within 500ps at SS/1.08/125
MEMORY SCRAMBLING:
The memory size is 8192 × 32 bits, so a total of 13 address bits (A12–A0) are required.
The higher address bits (A12–A4) are used for row selection through pre-decoding and post-decoding stages.
The pre-decoding is implemented using three 3:8 decoders, which divide the address bits into groups for efficient row decoding.
The lower address bits (A3–A0) are used for column decoding, corresponding to the MUX16 configuration.

## Slide 3: Possible pre-decoding stages
Specification / Stages | 2: 3x8 Decoder 1: 2x4 Decoder 1: 1x2 Decoder | 1: 3x8 Decoder 3: 2x4 Decoder | 1: 3x8 Decoder 2: 2x4 Decoder 2: 1x2 Decoder | 3: 3x8 Decoder
 | 22 output lines | 20 output lines | 20 output lines | 24 output lines
 | Total tapping = 512 | Total tapping = 448 | Total tapping = 476 | Total tapping = 192
Area
Power
3:3x8 decoder configuration is selected as it provides the best trade-off between area and power, achieving minimum power consumption with acceptable area overhead.

## Slide 4: 3:8 Pre-Decoder With Inverter Schematic
Gates | PMOS | NMOS
A1,A2,A3 | 1.35u | 0.55u
B | 2.03u | 1.5u
C | 5.6u | 1.5u
D | 4.5u | 4.5u
E | 8.0u | 3.4u
Sizing Using Logical Effort:

## Slide 5: 3:8 Pre-Decoder Schematic & Sizing
Sizing Using Logical Effort:
Gates | PMOS | NMOS
P | 0.378u | 0.140u
Q | 0.45u | 0.170u
R | 0.639u | 0.275u
S | 1.169u | 0.167u
T | 1.246u | 1.07u
U | 5.32u | 2.289u

## Slide 6: EZ Wave Simulation Results

## Slide 7: Column Decoder Schematic
BL Selection Box

## Slide 8: EZ Wave Simulation Results

## Slide 9: Pre Decoder: 3x8 Decoder Layout
Iteration 1
Area: 14.495*24.37 = 353.24 µm²

## Slide 10: Pre Decoder: 3x8 Decoder Layout
Iteration 2
Area: 34.79*8.25 = 287.01 µm²
Tri State Latch

## Slide 11: Pre Decoder: 3x8 Decoder Layout
DRC & LVS Clean Report

## Slide 12: Setup & Hold Time Waveform (3:8)
Waveform For Setup
Waveform For Hold

## Slide 13: Setup & Hold Time Results(3:8)
Input(ABC) | Setup Time(ps) | Hold Time (ps)
000 | 199.6 | -61.7
001 | 239.51 | -59.11
010 | 226.6 | -62.7
011 | 264.29 | -87.78
100 | 199.61 | -62.71
101 | 239.2 | -78.93
110 | 198.3 | -61.46
111 | 263.15 | -84.44
Delay in CLK w.r.t. External CLK at SS/1.08/125 = 53 ps
Delay in CLK w.r.t. External CLK at FF/1.32/-40 = 42 ps
Tristate Latch Hold Time
-17.7ps

## Slide 14: Column Decoder Layout
Area: 25.865*22.875 = 591.661µm²
DRC Report

## Slide 15: Column Decoder Layout
2X4 Decoder
Bitline Selection Box

## Slide 16: Challenges,Future Plan And Work Distribution
.
Challenges:
We had difficulty deciding the correct sizing of the column decoder and had to try multiple times.
We faced issues like LUP/dup DRC errors and sconnect problems, which made debugging and fixing the layout difficult.
We also faced difficulty in area optimization while using fingers in both the predecoder and column predecoder.
Future Plans:
Minimize layout areas to improve efficiency.
Focus on reducing delays for predecoder.
Aim to optimize PPA (Power,Performance,Area)
Work Distributions:
All three members were equally involved in all aspects of the work.

## Slide 17: THANK YOU!